## Slide 1
Finite Field Arithmetic
for Cryptography
Theory, Standards, and Hardware/Software Implementation
Modern Cryptography Series · Presentation 1 of 10
2025 | github.com/modern-cryptography

## Slide 2
Agenda
01
What is a Finite Field?
Algebraic foundations, groups, rings, and fields
02
GF(p) — Prime Fields
Modular arithmetic, properties, and examples
03
GF(2ⁿ) — Binary Extension Fields
Polynomial basis, irreducible polynomials, XOR arithmetic
04
Fields in Cryptographic Standards
AES (GF(2⁸)), ECC (P-256, Curve25519), and why they were chosen
05
Hardware Implementation
SoC / ASIC / FPGA architectures, Montgomery multiplication
06
SystemVerilog Examples
GF(2⁸) multiplier, modular arithmetic RTL
07
Python Examples
Galois field classes, ECC field arithmetic
08
Performance & Trade-offs
Comparison of approaches: LUT vs. combinational vs. pipelined

## Slide 3
What is a Finite Field?
Group
(G, +)
Closure, associativity, identity, inverses
Ring
(R, +, ×)
Group under + ; closure & associativity under ×
Field
(F, +, ×)
Ring where every non-zero element has a multiplicative inverse
Finite Field
GF(pⁿ)
A field with a finite number of elements. Exists iff |F| = pⁿ (p prime)
Key Properties of Finite Fields
Exists uniquely for every prime power pⁿ
Characteristic p: adding 1 to itself p times gives 0
GF(p): prime field — integers mod p
GF(pⁿ): extension field — polynomials mod irreducible poly
All arithmetic stays within the field (closure)
Every non-zero element has a multiplicative inverse
Named after Évariste Galois (1811–1832)
Foundation of AES, ECC, error-correcting codes, and more

## Slide 4
GF(p) — Prime Fields
GF(p) = { 0, 1, 2, …, p−1 } where p is prime
All operations are performed modulo p. Addition, subtraction, multiplication, and division (via modular inverse) all produce results within the field.
Example: GF(7) = { 0, 1, 2, 3, 4, 5, 6 }
+ | 0 | 1 | 2 | 3 | 4 | 5 | 6
0 | 0 | 1 | 2 | 3 | 4 | 5 | 6
1 | 1 | 2 | 3 | 4 | 5 | 6 | 0
2 | 2 | 3 | 4 | 5 | 6 | 0 | 1
3 | 3 | 4 | 5 | 6 | 0 | 1 | 2
4 | 4 | 5 | 6 | 0 | 1 | 2 | 3
5 | 5 | 6 | 0 | 1 | 2 | 3 | 4
6 | 6 | 0 | 1 | 2 | 3 | 4 | 5
Addition table mod 7
Prime Fields in Cryptography
P-256 (secp256r1)
p = 2²⁵⁶ − 2²²⁴ + 2¹⁹² + 2⁹⁶ − 1
TLS, ECDSA, ECDH
P-384 (secp384r1)
p = 2³⁸⁴ − 2¹²⁸ − 2⁹⁶ + 2³² − 1
Suite B, high-security TLS
P-521 (secp521r1)
p = 2⁵²¹ − 1 (Mersenne prime)
Highest NIST ECC security
Curve25519
p = 2²⁵⁵ − 19
X25519, Ed25519, Signal, WireGuard
Curve448
p = 2⁴⁴⁸ − 2²²⁴ − 1
X448, Ed448, ~224-bit security

## Slide 5
GF(2ⁿ) — Binary Extension Fields
Elements are polynomials over GF(2), i.e., binary coefficients {0, 1}
Arithmetic mod an irreducible polynomial of degree n. Addition = XOR, Multiplication = polynomial multiply + reduce.
GF(2⁸) — The AES Field
Irreducible polynomial (AES):
m(x) = x⁸ + x⁴ + x³ + x + 1
(hex: 0x11B)
256 elements — each is a byte (8 bits)
Addition example:
0x57 ⊕ 0x83 = 0xD4
(01010111 XOR 10000011 = 11010100)
Multiplication example:
0x57 × 0x83 = 0xC1 (mod m(x))
Multiply polynomials, reduce mod x⁸+x⁴+x³+x+1
Why Binary Extension Fields?
Addition = XOR → no carry propagation, single gate per bit
Maps naturally to digital hardware (bits = coefficients)
Constant-time operations → side-channel resistant
Efficient in both HW (LUT, shift-XOR) and SW (bitwise ops)
Used in AES, GCM, CRC, Reed-Solomon, McEliece

## Slide 6
Finite Fields in Cryptographic Standards
Standard | Field | Why This Field? | Used For
AES (Rijndael) | GF(2⁸) m(x)=x⁸+x⁴+x³+x+1 | Byte-oriented; XOR addition has no carry chain; efficient S-box via multiplicative inverse | Symmetric encryption (TLS, disk encryption, VPN)
AES-GCM | GF(2¹²⁸) m(x)=x¹²⁸+x⁷+x²+x+1 | Authentication tag via GHASH; 128-bit block matches AES; carry-less multiply (PCLMULQDQ) | Authenticated encryption (HTTPS, IPsec)
NIST P-256 (ECDSA/ECDH) | GF(p), p=2²⁵⁶−2²²⁴+2¹⁹²+2⁹⁶−1 | Pseudo-Mersenne prime enables fast reduction via shift/add; 128-bit security level | TLS certificates, code signing, FIDO2
Curve25519 (X25519/Ed25519) | GF(p), p=2²⁵⁵−19 | Near-Mersenne prime → single-word reduction; constant-time ladder; cofactor 8 | Signal, WireGuard, SSH, TLS 1.3
Curve448 (X448/Ed448) | GF(p), p=2⁴⁴⁸−2²²⁴−1 | Goldilocks prime: efficient Karatsuba; 224-bit security | High-security TLS, NIST SP 800-186
SM2 (Chinese std) | GF(p), 256-bit | National standard prime; similar structure to P-256 | Chinese gov encryption, digital signatures
Pseudo-Mersenne and Mersenne primes are preferred because reduction mod p becomes a series of additions and shifts — no general-purpose division needed.

## Slide 7
Why Were These Fields Chosen?
AES: Why GF(2⁸)?
Byte-oriented design
Each byte represents an element of GF(2⁸). This maps perfectly to 8-bit processor architectures and memory widths.
S-Box = Multiplicative Inverse
The AES S-box computes the multiplicative inverse in GF(2⁸) followed by an affine transformation. This provides optimal non-linearity and resistance to differential/linear cryptanalysis.
MixColumns = Matrix × Vector over GF(2⁸)
Each column is treated as a polynomial over GF(2⁸) and multiplied by a fixed polynomial c(x) modulo x⁴+1. This provides diffusion.
No carry propagation
Addition is XOR — constant-time, no carries, no branching. Ideal for both SW and HW.
ECC: Why Pseudo-Mersenne Primes?
Fast modular reduction
For p = 2²⁵⁵−19, reducing mod p requires only multiply by 19 and add — no general division. For P-256's structured prime, reduction uses shifts and additions.
Constant-time implementation
Curve25519 uses a Montgomery ladder that is inherently constant-time: every scalar bit executes the same operations. The prime 2²⁵⁵−19 allows this with efficient limb arithmetic.
Security margin
P-256 provides 128-bit security; P-384 provides 192-bit; P-521 (Mersenne prime 2⁵²¹−1) gives ~260-bit security. Curve25519 gives ~128 bits with superior performance.
Rigidity / Verifiability
Curve25519 uses the smallest prime ≡ 5 (mod 8) near 2²⁵⁶ → parameter choices are transparent and auditable.

## Slide 8
Hardware Implementation of FF Arithmetic
SoC / ASIC
Dedicated crypto accelerator blocks (AES-NI in x86 ISA)
Composite field decomposition: GF(2⁸) → GF(((2²)²)²) reduces gate count by ~20%
Montgomery multipliers with systolic arrays for ECC
Side-channel countermeasures: masking, dual-rail logic
Intel AES-NI: 53 Gbps native GF((2⁴)²) implementation in 45nm
FPGA
LUT-based S-box: ~32 LUTs per byte on modern Xilinx
Composite field S-box: Canright's method for compact design
Pipelined architectures: 7+ Gbps throughput
Block RAM for precomputed tables (256×8 for AES S-box)
DSP slices for large-field Montgomery multiplication
Software
Table-driven: 256-entry lookup for GF(2⁸) (cache-timing risk)
Bitsliced: process 64 blocks in parallel using 64-bit registers
SIMD: AVX2/NEON for parallel field ops
Carry-less multiply: PCLMULQDQ for GF(2¹²⁸) in GCM
Limb arithmetic: 5×51-bit or 10×25.5-bit for Curve25519

## Slide 9
Montgomery Multiplication for HW
Montgomery Modular Multiplication
Core Idea: Replace division by N with division by R (a power of 2)
MonPro(a, b, N):
Input: ã = aR mod N, b̃ = bR mod N
R = 2ⁿ (n = bit-width of N)
N' = -N⁻¹ mod R
t = ã × b̃
m = t × N' mod R
u = (t + m × N) / R
if u ≥ N: u = u − N
return u (= abR mod N)
Division by R = right-shift by n bits
mod R = mask lower n bits
→ No expensive modular division!
Hardware Architectures
Bit-Serial
Process 1 bit/cycle. Minimal area, n+1 cycles for n-bit operands. Used in constrained IoT SoCs.
Word-Serial (CIOS)
Process w-bit words. w×w multiplier + CSA. Balances throughput and area. Most common in FPGA ECC.
Systolic Array
Pipelined PEs pass partial products. High throughput with regular data flow. Ideal for ASIC.
Full-Parallel
Complete multiplication in 1 cycle. Enormous area but maximum throughput. Used in AES-NI accelerators.

## Slide 10
SystemVerilog: GF(2⁸) Multiplier
gf2_8_mult.sv
module gf2_8_mult (
input logic [7:0] a, b,
output logic [7:0] p
);
// AES irreducible poly: x^8+x^4+x^3+x+1
localparam [8:0] POLY = 9'h11B;
logic [7:0] partial [8];
// Bit-serial Russian peasant multiply
always_comb begin
partial[0] = a;
for (int i = 0; i < 8; i++) begin
// Accumulate if bit i of b is set
if (i == 0)
p = b[0] ? a : 8'h00;
else
p = p ^ (b[i] ? partial[i] : 8'h00);
// xtime: shift left, reduce if MSB set
if (i < 7)
partial[i+1] = {partial[i][6:0],1'b0}
^ (partial[i][7] ?
POLY[7:0] : 8'h00);
end
end
endmodule
How It Works
Russian Peasant Algorithm
Classic shift-and-add multiplication adapted for GF(2ⁿ). Process one bit of the multiplier per iteration.
xtime Operation
Left-shift by 1 (multiply by x). If MSB was 1, XOR with the reduction polynomial to keep the result in the field.
Irreducible Polynomial
0x11B = x⁸+x⁴+x³+x+1 is the AES standard polynomial. Ensures GF(2⁸) has 256 unique elements.
Combinational Logic
Fully unrolled — no clock needed. Synthesizes to ~100-150 gates. Can be pipelined for higher throughput.
Applications
Used in AES MixColumns (multiply by 02, 03) and S-box (multiplicative inverse via Itoh-Tsujii).

## Slide 11
SystemVerilog: Modular Arithmetic for GF(p)
mod_arith.sv — Parameterized modular add/sub
module mod_add #(
parameter WIDTH = 256
)(
input logic [WIDTH-1:0] a, b, p,
output logic [WIDTH-1:0] sum
);
logic [WIDTH:0] temp; // 1 extra bit
always_comb begin
temp = a + b;
sum = (temp >= {1'b0, p})
? temp - p : temp[WIDTH-1:0];
end
endmodule
module mod_sub #(
parameter WIDTH = 256
)(
input logic [WIDTH-1:0] a, b, p,
output logic [WIDTH-1:0] diff
);
always_comb begin
if (a >= b)
diff = a - b;
else
diff = p - (b - a);
end
endmodule
Design Notes
Parameterized Width
WIDTH parameter allows the same module for 256-bit (P-256), 255-bit (Curve25519), 384-bit (P-384), etc.
Conditional Reduction
After addition, if result ≥ p, subtract p once. This works because inputs are in [0, p−1], so a+b < 2p.
Carry Bit
Extra bit in temp catches overflow from the addition. Essential for correctness when a+b > 2^WIDTH.
Timing Considerations
Wide adders/comparators have long carry chains. For ASIC/FPGA, consider carry-save or redundant representations to meet timing.
Side-Channel Warning
The conditional subtract creates data-dependent timing. For production crypto, use constant-time techniques (always compute both paths, select via MUX).

## Slide 12
Python: Finite Field Arithmetic
gf2_8.py — GF(2⁸) for AES
class GF2_8:
"""Galois Field GF(2^8) with AES poly."""
POLY = 0x11B # x^8+x^4+x^3+x+1
def __init__(self, val):
self.val = val & 0xFF
def __add__(self, other): # XOR
return GF2_8(self.val ^ other.val)
def __mul__(self, other):
a, b, p = self.val, other.val, 0
for _ in range(8):
if b & 1:
p ^= a
hi = a & 0x80
a = (a << 1) & 0xFF
if hi:
a ^= self.POLY & 0xFF
b >>= 1
return GF2_8(p)
def inverse(self): # Fermat: a^254
r = GF2_8(1)
base = GF2_8(self.val)
for bit in bin(254)[2:]:
r = r * r
if bit == '1':
r = r * base
return r
# Example
a = GF2_8(0x57); b = GF2_8(0x83)
print(f"{a*b} => 0x{(a*b).val:02X}")
print(f"inv(0x57) = 0x{a.inverse().val:02X}")
gf_p.py — GF(p) for ECC
class GFp:
"""Prime field GF(p) element."""
def __init__(self, val, p):
self.val = val % p
self.p = p
def __add__(self, o):
return GFp(self.val + o.val, self.p)
def __sub__(self, o):
return GFp(self.val - o.val, self.p)
def __mul__(self, o):
return GFp(self.val * o.val, self.p)
def __truediv__(self, o):
return self * o.inverse()
def inverse(self): # Extended Euclidean
return GFp(pow(self.val, self.p-2,
self.p), self.p)
def __repr__(self):
return f"GFp({self.val})"
# Curve25519 prime field
p25519 = 2**255 - 19
a = GFp(42, p25519)
b = GFp(17, p25519)
c = a * b / a # should return 17
print(f"a*b/a = {c}")
# P-256 prime
p256 = 2**256 - 2**224 + 2**192
+ 2**96 - 1
x = GFp(123456789, p256)
print(f"x^(-1)*x = {x.inverse() * x}")

## Slide 13
Performance & Trade-offs
Chart: AES-128 Throughput by Implementation
| SW (OpenSSL) | FPGA LUT S-box | FPGA Composite | FPGA Pipelined | ASIC (45nm)
Throughput (Gbps) | 3.2 | 5.5 | 7 | 21.5 | 53
Sources: Canright (2005), McCanny (2003), Mathew/Intel (2011)
Implementation Trade-offs
Approach | Area | Speed | Side-Ch.
LUT / Table-based | High (RAM) | Moderate | Cache-timing risk
Composite Field | Low (~80 gates) | Moderate | Good
Pipelined Composite | Medium | Very High | Good
Bit-sliced (SW) | N/A (registers) | High | Excellent
Full-parallel ASIC | Very High | Maximum | Excellent
The fundamental trade-off: area vs. throughput vs. side-channel resistance. Composite-field decomposition gives the best area efficiency; pipelining maximizes throughput; bit-slicing / constant-time algorithms provide side-channel resistance. Production systems must balance all three.

## Slide 14
Key Takeaways
1
Finite fields are the algebraic foundation of nearly all modern cryptography — from AES to ECC to post-quantum schemes.
2
Two families dominate: GF(2ⁿ) for symmetric ciphers and GF(p) for public-key / elliptic curve cryptography.
3
Field parameters are chosen for both security and implementation efficiency — Mersenne primes, carry-free XOR, etc.
4
Hardware ranges from minimal bit-serial designs (IoT) to 53+ Gbps ASIC accelerators (data centers).
5
Side-channel resistance is as important as raw performance — constant-time code is essential.
Further Reading & References
FIPS 197 (AES) · NIST SP 800-186 (ECC Curves) · RFC 7748 (Curve25519/448) · Kleppmann, "Implementing Curve25519" · Canright, "A Very Compact Rijndael S-box"

## Slide 15
Modern Cryptography Series
01
Finite Field Arithmetic
This presentation
02
Elliptic Curve Cryptography (ECC)
Coming next
03
AES — Design & Implementation
Planned
04
Hash Functions & MACs
Planned
05
Public Key Cryptography (RSA, DH)
Planned
06
Digital Signatures (ECDSA, EdDSA)
Planned
07
Post-Quantum Cryptography
Planned
08
Key Exchange Protocols
Planned
09
Side-Channel Attacks & Countermeasures
Planned
10
Crypto Hardware Accelerator Design
Planned
github.com/modern-cryptography | Contributions welcome!